## Slide 1: P4Runtime, and PSA types with target-specific sizes
Andy Fingerhut
This version last updated: May 16, 2018
(Original version: March 21, 2018)

## Slide 2
P4Runtime control protocol uses gRPC
  Serialization into bytes uses Google Protocol Buffers
  Transport method between controller and agents is likely HTTP / TCP / etc.
  Values of type bit<17> in P4 program will be serialized with padding up to whole number of bytes, but P4Info file will contain bit<17> type, not bit<24>. Controller software needs to know the data plane has 17-bit width, to know legal range of values possible.
  PSA types with target-specific widths will have widths defined by P4Runtime or PSA spec, wide enough for all PSA targets, e.g. 32 bits for port ids.
Agent software speaks P4Runtime to controller
  But it has a large portion of its code that is very specific to target device.
  If target is an ASIC / FGPA / NPU, typically agent will run on a general purpose CPU on the same board as target, and use something like PCIe interface to do register reads and writes and DMA to the target.
  Target X Agent knows how to numerically translate 32-bit control plane port values to/from target X 7-bit PortId_t values.
Controller
(P4Runtime client)
(P4Runtime server)
Target X Agent
Target X Data plane
PortId_t size is 7 bits
P4Runtime protocol
port id size is 32 bits
(P4Runtime server)
Target Y Agent
Target Y Data plane
PortId_t size is 15 bits
Target-specific communication (e.g. PCIe, Ethernet)

## Slide 3: What agents touch #1
Agents handle these
  Table add/delete/modify
    Table key fields and action parameters
  parser value set add/del
  Digest message contents
    Rationale: Batch many small messages into larger messages to reduce message rate to controller
  Register read/write
    Register data contents, and nice if they support structs here, too, like Digest messages will.
    Translate index values?
  Indexed Counter and Meter config/read/etc.
    Translate index values?
Agent also handles these
  P4Runtime PacketOut – these become packets received by PSA device on input port PSA_PORT_CPU
  P4Runtime PacketIn - packets sent by PSA device to output port PSA_PORT_CPU become these
  These packets traverse the same gRPC session between controller and agent that other P4Runtime messages do.
  Thus agent can do translation of header fields.
  See next slide for a different packet case.
Controller
(P4Runtime client)
(P4Runtime server)
Target X Agent
Target X Data plane
PortId_t size is 7 bits
P4Runtime protocol
port id size is 32 bits
(P4Runtime server)
Target Y Agent
Target Y Data plane
PortId_t size is 15 bits
Target-specific communication (e.g. PCIe, Ethernet)

## Slide 4: What agents touch #2
PSA externs that are not affected by numerical translation/size issues:
  DirectCounter, DirectMeter, Hash, Checksum, Random, ActionProfile, ActionSelector
Agents do not handle direct data plane to data plane packets
  This includes any packets between targets and controller that do not go through P4Runtime PacketIn / PacketOut service.
  P4Runtime and PSA do not prevent you from transmitting packets in this way – they just do not (in v1.0) define a way to do numerical translation of PortId_t and other types. Maybe v1.x will do so.
Control plane things that a P4 compiler does not need to know about
  Any control plane APIs for configuring port up/down/settings, or Packet ReplicationEngine APIs.
  Agent needs to know about any port translation or other target specific things there, but that is independent of any P4 program.
Controller
(P4Runtime client)
(P4Runtime server)
Target X Agent
Target X Data plane
PortId_t size is 7 bits
P4Runtime protocol
port id size is 32 bits
(P4Runtime server)
Target Y Agent
Target Y Data plane
PortId_t size is 15 bits
Target-specific communication (e.g. PCIe, Ethernet)

## Slide 5: Goals
Enable writing a P4_16 source program myp4prog.p4 that does #include “psa.p4” near the top, and can be compiled to multiple target devices
  without requiring changes to myp4prog.p4 for each target.
For port ids, different targets want to customize the size of type PortId_t in the data plane.
  e.g. maybe vendor device X wants a 7-bit wide value in the data plane for PortId_t, but vendor device Y wants a 15-bit wide value.
  Vendor device X does not want to waste 15-7=8 bits to store a PortId_t in the data plane implementation of P4 programs, just because some other vendor device wants to use that many bits.
As far as possible, controller software does not want to know about these differences.
  It does need to somehow discover and restrict itself to using the physical ports that actually exist on each device, but that does not imply that it needs to know about the custom sizes in the data plane mentioned above.
PortId_t is one example type used in these slides, but there are other similar types defined in PSA.
  PSA v1.0 defines 7 types that are expected to be customized by different vendors
  For the complete list, see: https://p4.org/p4-spec/docs/PSA-v1.0.0.html#sec-psa-type-definitions
  Currently 2 of them are special in that we expect numerical translation to occur between the controller software and the data plane. These are PortId_t and ClassOfService_t. Maybe also this will be done for Timestamp_t values.

## Slide 6: Goals (2)
The P4Runtime wants a P4Info file, auto-generated from myp4prog.p4, that tells a controller most or all of what it needs to know to communicate with a target device that has that P4 program installed into it.
  e.g. if a P4_16 program has a table key with a field named my_funky_field that is type bit<17> in it, P4Info should indicate that the field is type bit<17>.
  For cases where the bit width is explicitly given in myp4prog.p4, both the target-specific data plane implementation and P4Info should reflect that, and the controller will thus be aware of that size. This is expected and normal.
  The potentially tricky part is for the values that the data planes want to have target-specific sizes for.
Generate the target-specific compiled versions (i.e. “binary blobs”) of a P4 program from myp4prog.p4 and the psa.p4 #include file.
  Note: It is OK if psa.p4 is mostly the same, but has target-specific customizations in it. Each vendor will ship its customized psa.p4 file with its target-specific compiler.
Generate the P4Info file from myp4prog.p4, too
  Perhaps in the same compilation run as the target-specific binary blob is created, or it could be a separate invocation of the P4 compiler.
  The P4Info file contents should ideally be identical, regardless of the target device. It should be a function only of myp4prog.p4, regardless of any differences that might exist in target-specific psa.p4 files.
Minimize the number of annotations required in the P4 source code file myp4prog.p4 in order to achieve these goals.

## Slide 7
If you disagree with any of the goals, then you can stop here. We should first agree on a set of goals.

## Slide 8: One potential approach
Let each vendor create customized psa.p4 files that they ship with their compiler.
  They contain whatever details are needed so that their compiler will generate target-specific binary blobs that customize the bit widths of values with type PortId_t.
  Other than that, the psa.p4 files for different targets are likely to be very similar.
  Note: #include <stdio.h> pulls in somewhat different files for different combinations of (operating system version, C library version, C compiler and version).
    These differences are mostly in things like annotations, and rarely cause troubles.
    When such differences do cause troubles, they are treated as bugs and fixed.
    I would expect the same for target-specific variations in the psa.p4 file.
When a P4Info file is generated from myp4prog.p4, every value of type PortId_t should be described as having size 32 bits.
  Note: This value 32 would be common to _all_ PSA implementations. Every P4 compiler that can generate a P4Info file would know about it, somehow.
  If 32 is not big enough, we should pick a number we can all agree on really, really soon. One that will last a long time, e.g. for the expected lifetime of PSA.

## Slide 9: One potential approach (2)
Result:
  Target X binary blobs will use only 7 bits wherever type PortId_t values appear, but target Y binary blobs will use 15 bits wherever that type appears.
  P4Info file will use 32 bits wherever that type appears.

## Slide 10: Restrictions on writing P4 code
I strongly recommend reading all of this section of the PSA spec.
  https://p4.org/p4-spec/docs/PSA-v1.0.0.html#sec-data-plane-vs-control-plane-values
  It is about 1-2 pages long. It won’t take long to read, really.
Another recommendation: Never use hard-coded numeric literal values like 0xfff when comparing values of PortId_t (or the other 6 ‘special’ PSA types), or assigning values to them.
  Instead, limit yourself to obtaining their values from action parameters with values installed by the control plane
  PSA v1.0 defines a named constants that are perfectly fine to use for a couple of special ports:
    PSA_PORT_CPU – the port to/from the CPU
    PSA_PORT_RECIRCULATE – the port to send packets to when you want to recirculate them

## Slide 11: Open issues
How to minimize the annotations needed in a P4_16 program myp4prog.p4 to achieve these effects?
  Ideally such annotations could be limited to only the target-specific psa.p4 file, and need not be sprinkled throughout myp4prog.p4.
  The current open source p4c compiler does not enable this.
    I have created this issue for p4c asking how this might be done.
    https://github.com/p4lang/p4c/issues/1157
    If you think this issue is important, put your +1 or comment on that issue, or convince your representative to the P4_16 language working group to beat the drum on it until it is resolved.
    Mihai Budiu’s suggestion of introducing in P4_16 syntax like “newtype bit<7> PortId_t” instead of using “typedef” may be a fruitful approach to take there.
What if my myp4prog.p4 tries to add two values of PortId_t?
  Because of the additional PSA property of there being controller <-> data plane translation of numeric values involved, that is likely a non-portable thing to do that will not lead to happiness.
  Should P4 compilers be required to treat such attempts as errors? Maybe that would be nice to have. Beat on that drum, too, if you care strongly enough about it. The PSA section linked on previous slide already says not to do it, but not everyone reads such things, I know.

## Slide 12: Open issues (2)
Should controller software be able to name PSA_PORT_CPU and PSA_PORT_RECIRCULATE values in target-independent way?
  Seems useful. Seems like there should be a straightforward way to do this.
Potential quick hack:
  To generate P4Info file, compile with a psa.p4 file that has “typedef bit<32> PortId_t;”, the size in bits that you want PortId_t values to be between controllers/clients and agents/servers.
  I do not think this is a good long term approach, because for the 2 PSA types with numerical translation, PortId_t and ClassOfService_t, we still want to minimize annotations in P4 program myp4prog.p4 wherever those types are used, ideally 0 of them.

## Slide 13: PSA Digest extern generation
Digest and Register data value types are explicit part of object instantiation
Proposal: Regardless of the expressions in the method calls for these objects, use the type definition from the object instantiation, including the types of any fields in a struct.
Could be arbitrarily deep nested struct/etc. if P4Info supports that.
Currently p4c uses the names in the list expression to generate P4Info, disallowing expressions or constants.
struct mac_learn_digest_t {
PortId_t port;
bit<48> srcAddr;
}
control DeparserImpl ( … ) {
﻿ Digest<mac_learn_digest_t>() mac_learn_digest;
apply {
mac_learn_digest.pack({ meta.learn_port, meta.learn_srcAddr });
}
}

## Slide 14: Rules for types of expression

## Slide 15: Determining types of expressions – idea #1
PortId_t values support all operations that values of type bit<X> do, but only with other values of type PortId_t, not with values of type bit<X>
Deriving type of expression that includes PortId_t types becomes easy for compiler
  (PortId_t <binary_op> PortId_t) and (<unary_op> PortId_t) are always type PortId_t.
  (PortId_t <binary_op> bit<X> value) is compiler error, even if they are same bit width
  (PortId_t <binary_op> ClassOfService_t) is compiler error, even if they are same bit width
Values of type bit<X> and PortId_t can be cast to each other.
  This does not cause any change in the bit pattern in the data plane – the cast is just to keep the types separate from each other, to make expression type derivation straightforward.
  Lets you do potentially wrong things if you really want to, as long as you use the right casts:
    (my_port + 1) is compiler error, but (my_port + (PortId_t) 1) compiles and does the thing you would expect with the bit patterns, and has type PortId_t.
    (my_port == (PortId_t) 1) would be not a compiler error, but maybe a lint tool warning.
    Should there be a “PortIdBaseType_t” cast auto-created from ”newtype” definition.
  Some potentially functionally wrong things don’t require casts, e.g. (my_portid1 + my_portid2).
    The compiler can’t stop you from writing functional errors in all cases. I don’t think anyone should reasonably expect a compiler to catch all possible functional errors (or even many of them).
These ideas align well with the “newtype bit<7> PortId_t;” proposal.

## Slide 16: Determining types of expressions – idea #2
PortId_t values support all operations that values of type bit<X> do, including with other unsigned values of same bit width
  (PortId_t <binary_op> PortId_t) and (<unary_op> PortId_t) are always type PortId_t. OK
  What type should (PortId_t <binary_op> bit<X> value) be?
  What type should (PortId_t <binary_op> ClassOfService_t) be?
I do not see how to make this idea work in any desirable way.
  How would you mark PortId_t values specially in P4Info file for control plane, but not also values of type bit<7>, which happen on some platforms to be same bit width as PortId_t?

## Slide 17: Categories of control plane types
 | Data and control plane sizes identical. Control plane may use custom syntax for input/output (e.g. IPv4Address_t) | Per-target custom data plane size, but no numerical translation (e.g. MulticastGroup_t, CloneSessionId_t, PacketLength_t, EgressInstance_t) | Per-target custom data plane size, and numerical translation between control and data planes (e.g. PortId_t, ClassOfService_t, Timestamp_t)
Numerical translation in agent? | No | No | Yes
Data plane size in bits can be different than control plane size? | No | Yes | Yes
Agent should check and return error if controller value is invalid? | No – all possible values for the type should be considered OK by the agent. | Yes – MulticastGroup_t might have a range of valid values that is not a power of 2, e.g. [0, 12K-1]. A controller attempting to use 12K+5 should give error. | Yes – Valid 32-bit PortId_t values in control plane might be arbitrary subset of possible bit patterns, and agent should return error if controller attempts to use unsupported value.
Useful to do arithmetic on values in data plane? | Yes | Yes, addition, subtraction, < <= > >= for PacketLength_t. Less clear how useful for other types. | Maybe in a few unusual circumstances
Useful to do binary operations with bit<W> types of same width? | Yes, e.g. bitwise AND with constant or run-time variable masks. | Yes, add/subtract constant for calculating new packet lengths when adding/removing headers. | Maybe in a few unusual circumstances.
Useful to do ternary or LPM matching? | Yes | Maybe, e.g. ternary on PacketLength_t could be used for packet length ranges. | Maybe for Timestamp_t, where numerical translation is “linear”. Seems unlikely for PortId_t or ClassOfService_t where translation is arbitrary.

## Slide 18: Planned approach for control plane types
Add ‘type’ to P4_16 language specification:
  e.g. ‘type bit<7> PortId_t;’ creates a new type that is like bit<7>, but not the same type as bit<7>
  You can do arithmetic operations on two PortId_t values without needing casts, e.g. (port1 + port2)
    TBD: Some might wish for P4 compiler to warn if you do arithmetic operations on PSA types that have numerical translation like PortId_t and ClassOfService_t.
  If you find a need for it, you can cast between PortId_t and PortIdBitVector_t, where PortIdBitVector_t is bit<7>, defined as ‘typedef bit<7> PortIdBitVector_t;’ in psa.p4.
PSA will contain definitions like this for each of 7 types:
  type bit<7> PortId_t; // This will be used most often
  typedef bit<7> PortIdBitVector_t; // only if you want to cast to a bit<7>
  typedef bit<32> PortIdInHeader_t; // for headers to/from agent on PSA CPU port

## Slide 19: Planned approach for control plane types (#2)
P4 compiler will preserve type name ‘PortId_t’ from source code when generating P4Info files, when used as:
  Table key field
  Action parameter
  Field of struct for Digest or Register extern
  Perhaps other places I am forgetting right now
These 7 type names will be ‘special’ for the PSA architecture.
  They can be used for different or similar purposes in other P4_16 architectures.